## Slide 1: Manycore Network Interfaces for In-Memory Rack-Scale Computing
Alexandros Daglis, Stanko Novakovic,
Edouard Bugnion, Babak Falsafi, Boris Grot

## Slide 2: In-Memory Computing for High Performance
Tight latency constraints  Keep data in memory
Need large memory pool to accommodate all data
Data

## Slide 3: Nodes Frequently Access Remote Memory
Need fast access to both small and large objects in remote memory
Graph Serving
Fine-grained access
Graph Analytics
Bulk access

## Slide 4: Rack-Scale Systems: Fast Access to Big Memory
Large memory capacity, low latency, high bandwidth
Vast memory pool in small form factor
On-chip integrated, cache-coherent NIs
Examples: QPI, Scale-Out NUMA [Novakovic et al., ‘14]
High-performance inter-node interconnect
NUMA environment
Low latency for fine-grained transfers
High bandwidth for bulk transfers

## Slide 5: Remote Memory Access in Rack-Scale Systems
NI
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
NI
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
: Bandwidth-critical
Interaction with cores
Data transfer
NI
NI
Network
Integrated NIs
Interaction with cores via memory-mapped queues
Directly access memory hierarchy to transfer data
: Latency-critical

## Slide 6: Network Interface Design for Manycore Chips
NI placement & design is key for remote access performance
Obvious NI designs suffer from poor latency or bandwidth
  Contributions
NI design space exploration for manycore chips
Seamless integration of NI into chip’s coherence domain
Novel Split NI design, optimizing for both latency and bandwidth
This talk: Low-latency, high-bandwidth NI design for manycore chips

## Slide 7: Outline
Overview
Background
NI Design Space for Manycore Chips
Methodology & Results
Conclusion

## Slide 8: User-level Remote Memory Access
RDMA-like Queue-Pair (QP) model
Cores and NIs communicate through cacheable memory-mapped queues
Work Queue (WQ) and Completion Queue (CQ)
core
poll
CQ
write
write
WQ
poll
soNUMA: Remote memory access latency ≈ 4x of local access
Local node
Remote node
Inter-node
network
Direct memory
access
NI
NI

## Slide 9: Implications of Manycore Chips on Remote Access
NI capabilities have to match chip’s communication demands
More cores  Higher request rate
Straightforward approach: scale NI across edge
Close to network pins
Access to NOC’s full bisection bandwidth
Caveat: Large average core to NI distance
Significant impact of on-chip interactions on end-to-end latency
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c
c

## Slide 10: Edge NI 4-Cache-Block Remote Read
QP interactions account for up to 50% of end-to-end latency
Network Router
QP
dir
Data handling
NI unrolls to cache-block-sized requests
Outgoing requests
Incoming replies
Data transfer completed. Repeat QP interactions to write CQ
$
$
Core writes WQ
NI reads WQ
QP interactions
NI writes CQ
Core reads CQ
Bandwidth ✓
Latency ✗
LLC
NOC router
core
dir

## Slide 11: NI Design Space
Bandwidth
Latency
Target
Edge NI

## Slide 12: Reducing the Latency of QP Interactions
Collocate NI logic per core, to localize all interactions
  Still have coherence directory indirection 
$
$
QP
dir
core

## Slide 13: Reducing the Latency of QP Interactions
Collocate NI logic per core, to localize all interactions
  Still have coherence directory indirection 
Attach NI cache at core’s L1 back side
  Similar to a write-back buffer
  Transparent to coherence mechanism
  No modifications to core’s IP block
Localized QP interactions: latency of multiple NOC traversals avoided!
$
$
core


## Slide 14: Per-Core NI 4-Cache-Block Remote Read
Network Router
All QP interactions local!
Data handling
Outgoing requests

## Slide 15: Per-Core NI 4-Cache-Block Remote Read
Network Router
Minimized latency but bandwidth misuse for large requests
All reply packets received!
Write CQ locally
Data handling
Incoming replies
Write payload in LLC
Bandwidth ✗
Latency ✓

## Slide 16: NI Design Space
Bandwidth
Latency
Target
Per-core NI
Edge NI

## Slide 17: How to Have Your Cake and Eat It Too
Insight:
QP interactions best handled at request’s initiation location
Data handling best handled at the chip’s edge
Split NI addresses the shortcomings of Edge NI and Per-core NI
Communication
via NOC packets
Solution: The two can be decoupled and physically separated!
NI Frontend
QP interactions
Data handling
Network packet handling
NI Backend
QP interactions
Data handling
Network packet handling

## Slide 18: Split NI 4-Cache-Block Remote Read
Network Router
All QP interactions local!
All reply packets received!
Write CQ locally
Data handling
Outgoing requests
Incoming replies
Both low-latency small transfers and high-bandwidth large transfers
Bandwidth ✓
Latency ✓

## Slide 19: NI Design Space
Bandwidth
Latency
Target
Per-core NI
Edge NI
Split NI

## Slide 20: Methodology
Case study with Scale-Out NUMA [Novakovic et al., ‘14]
State-of-the-art rack-scale architecture based on a QP model
Cycle-accurate simulation with Flexus
Simulated single tiled 64-core chip, remote ends emulated
Shared block-interleaved NUCA LLC w/ distributed directory
Mesh-based on-chip interconnect
  DRAM latency: 50ns
Remote Read microbenchmarks
Data exceeds LLC capacity

## Slide 21: Application Bandwidth
Split NI: Maximized useful utilization of NOC bandwidth
Chart: Transfer size (Bytes)
| 64.0 | 128.0 | 256.0 | 512.0 | 1024.0 | 2048.0 | 4096.0 | 8192.0
Edge NI | 63.223 | 113.1575 | 186.4144 | 202.7267 | 209.8612 | 212.4217 | 213.8458 | 214.2787
Per-core NI | 158.835 | 145.6548 | 116.3915 | 110.0349 | 70.1617 | 62.9016 | 62.7862 | 57.4307
Split NI | 150.1634 | 177.2185 | 189.1501 | 196.8936 | 202.29 | 211.3001 | 213.0687 | 213.6249
Peak available bandwidth (256GBps)

## Slide 22: Latency Results for Single Network Hop
Chart: Transfer size (Bytes)
| 64.0 | 128.0 | 256.0 | 512.0 | 1024.0 | 2048.0 | 4096.0 | 8192.0
Edge NI | 364 | 365 | 367.5 | 374 | 392.5 | 418.5 | 476 | 599
Per-core NI | 225 | 227.5 | 230.5 | 236.5 | 254.5 | 285 | 357 | 516.5
Split NI | 227 | 228 | 231 | 240 | 256.5 | 290.5 | 350.5 | 466.5
Ideal | 201.5 | 202.5 | 205.5 | 214.5 | 231 | 265 | 325 | 441
Split NI: Remote memory access latency within 13% of ideal
Network roundtrip latency (70ns)

## Slide 23: Conclusion
NI design for manycore chips crucial to remote memory access
Fast core-NI interaction critical to achieve low latency
Large transfers best handled at the edge, even in NUMA machines
Per-Core NI: minimized cost of core-NI interaction
Seamless core-NI collocation, transparent to chip’s coherence
Split NI: low-latency, high-bandwidth remote memory access
  Non-intrusive design – No modifications to core’s IP block

## Slide 24: Thank you! Questions? http://parsa.epfl.ch/sonuma