## Slide 1: SABRes: Atomic Object Reads for In-Memory Rack-Scale Computing
Alexandros Daglis
Dmitrii Ustiugov, Stanko Novakovic
Edouard Bugnion, Babak Falsafi, Boris Grot

## Slide 2: Online Services
  Massive datasets, immense reader concurrency
Powered by datacenters
PBs of data, millions of users
Mostly reads, occasional writes
write
reads

## Slide 3: Remote Memory Access
  One-sided operations do not provide object read atomicity
Frequent remote memory accesses within datacenter
Networking traditionally expensive
RDMA technology
Fast one-sided ops
Object semantics
Need to read objects atomically
Application
NI
CPU
NI
CPU
zZz
Memory
Memory

## Slide 4: Object Atomicity in Software
One-sided ops’ atomicity limited to single cache line
Object atomicity provided by SW: embedded metadata
SW checks expensive: up to 50% of a remote object read!
  SABRes: minimal NI extensions, up to 2x faster object reads
Network
post-transfer atomicity check by CPU
NI
CPU
Memory
object
M
NI
CPU
Memory
object
M
zZz

## Slide 5: Outline
Overview
Background
SABRes design
Results
Summary

## Slide 6: Modern Distributed Object Stores
Infrequent writes (over RPC)
Optimistic one-sided reads (RDMA)
Rare conflicts (read-dominated workloads)
High concurrency & fast remote memory accesses
Software mechanisms for object read atomicity
Hardware does not provide one-sided atomic object reads
Examples: Pilaf [Mitchell’13], FaRM [Dragojevic’14, ’15]
  SW mechanisms enable concurrent atomic object reads

## Slide 7: State-of-the-art Atomic Reads
CPU checks versions & copies
(Same for LOCAL accesses!)
Cache-line versions
Object layout in memory
Application data
Per-cache-line versions (FaRM [Dragojevic’14,’15])
CPU
NI
CPU
NI
Source: Server A
Destination: Server B
✗ CPU overhead for version embedding/stripping
✗ Intermediate buffering for all reads & writes
Memory
Memory
✓
✓
✓
✓
writer
2
2
2
2
3
3
3
3
3
3
3
3

## Slide 8: Emerging Networking Technologies
RDMA
Lean user-level protocol
High-performance fabrics
One-sided ops
Scale-Out NUMA [ASPLOS’14]
All the above
Tight integration – On-chip NI
  Faster remote memory access exacerbates SW overheads
RDMA
Object read latency
Transfer
SW atomicity
15%
soNUMA
50%

## Slide 9: Software Atomicity Overhead
soNUMA: remote access latency ~4x of local [ASPLOS’14]
FaRM KV store
ARM Cortex-A57 cores
  Need hardware support for object atomicity
Chart: Object size (B)
| 128.0 | 256.0 | 512.0 | 1024.0 | 2048.0 | 4096.0 | 8192.0
transfer | 0.2573 | 0.2626 | 0.2872 | 0.3031 | 0.3333 | 0.453 | 0.6071
framework+application | 1.2353 | 1.2094 | 1.2401 | 1.2742 | 1.3212 | 1.2598 | 1.4777
version stripping | 0.1517 | 0.1812 | 0.2395 | 0.3738 | 0.5972 | 1.0762 | 1.9533
Up to 50%
Transfer is small fraction

## Slide 10: Design Goals
Low latency & high throughput
Low single-transfer latency, high inter-transfer concurrency
Lightweight HW support
Small hardware footprint
Detect atomicity violations early
Unlike post-transfer checks of SW solutions
  Can meet goals with hardware extensions in NI

## Slide 11: Towards Hardware Atomic Reads
Leverage NI’s coherent on-chip integration
  Detect atomicity violations
End-to-end guarantees: objects are structured SW constructs
  Range of consecutive addresses
  Object header w/ version
  Writers always increment version before & after data update
Version
Data
Data
Data
  HW SW co-design for efficient hardware
Last-level cache
NI
CPU
Inter-node network
Memory

## Slide 12: SABRes: Atomic Remote Object Reads in Hardware
Memory hierarchy
data replies
Object 0
…
MMU
read cache lines
requests
Invalidation
Controller logic
One-sided ops controller at destination
Inter-node network
Remote reads
Local writes
Object 1
Object N
Invalidation
Address tracking
Memory hierarchy
data replies
Object 0
…
MMU
read cache lines
requests
Invalidation
Controller logic
One-sided ops controller at destination
Inter-node network
Remote reads
Local writes
Our goal: Simple hardware for zero-overhead atomic object reads
Object 1
Object N
Invalidation
Address tracking
Remote read
NI
logic
Leverage: - “version+data” object layout
CPU
NI
Network
  Serialized version/data reads increase latency
Memory
LLC
read version
1
2
read data
3
Re-read version
& compare
write
VERSION MISMATCH
 ABORT!
Reply (data or abort)

## Slide 13: SABRes: Atomic Remote Object Reads in Hardware
Memory hierarchy
data replies
Object 0
…
MMU
read cache lines
requests
Invalidation
Controller logic
One-sided ops controller at destination
Inter-node network
Remote reads
Local writes
Object 1
Object N
Invalidation
Address tracking
Memory hierarchy
data replies
Object 0
…
MMU
read cache lines
requests
Invalidation
Controller logic
One-sided ops controller at destination
Inter-node network
Remote reads
Local writes
Our goal: Simple hardware for zero-overhead atomic object reads
Object 1
Object N
Invalidation
Address tracking
Remote read
NI
logic
CPU
  Simple hardware, atomicity w/ zero latency overhead
Memory
LLC
Leverage: - “version+data” object layout
- Coherent NI integration & object address contiguity
Speculatively
read version & data
Address range tracking
write
ABORT!
invalidation
Network

## Slide 14: Address Range Tracking Implementation
NI
logic
Network
Object 0
…
Object 1
Object N
Stream buffers
read cache lines
…
Free
Used (awaiting reply from memory)
Completed (memory reply received)
Object read (6 cache lines)
data replies
invalidation
CONFLICT – ABORT!
  Speculation: no serialization & early conflict detection
  -
  >
base
  -
  >
base
  -
  >
base
Reply (abort)
Send payload back to requester
Memory
LLC
Stream buffer entry state:

## Slide 15: FaRM KV Store on soNUMA
SABRes w/ 16 32-entry stream buffers  35-52% lower E2E latency
Remove SW atomicity check overhead
Remove intermediate buffer management
  Latency reduction  commensurate throughput improvements
Chart: E2E latency (μs)
transfer | 0.2573 | 0.2414 | 0.2626 | 0.2427 | 0.2872 | 0.2458 | 0.3031 | 0.2781 | 0.3333 | 0.3165 | 0.453 | 0.4167 | 0.6071 | 0.5928
system + app | 1.014 | 0.7665 | 1.0426 | 0.7688 | 1.0615 | 0.8202 | 1.2742 | 1.0288 | 1.3212 | 1.0761 | 1.2598 | 1.2058 | 1.4777 | 1.3484
version stripping | 0.1517 | 0 | 0.1812 | 0 | 0.2395 | 0 | 0.3738 | 0 | 0.5972 | 0 | 1.0762 | 0 | 1.9533 | 0

x-axis | 0 | 0 | 0 | 0 | 0 | 0 | 0
SABRes
SW atomicity

## Slide 16: Summary
Software object atomicity mechanisms increasingly more costly
SABRes: lightweight NI extensions for atomic remote object reads
Up to 2x latency & throughput benefit for distributed object stores

## Slide 17: Thank you! Questions?
For more information please visit us at
parsa.epfl.ch/sonuma